## Slide 1: Smoothing experimental data
May 4, 2026

## Slide 2
Overview
When (not) to smooth your data?
Know your noise
Different smoothers
  Window methods: Convolution, Savitzky Golay
  Total variation methods (e.g. Whitaker-Eilers)
Discussion

## Slide 3
When (not) to smooth your data
NO: direct interpretation or fitting
  You may miss features because of (excessive) smoothing
  You may see features that are not there because of smoothing of an outlier
YES: Further transformation
  Fourier transformation
  Derivative
  Presentation?
Would you smooth these XRD spectra?

## Slide 4
Know your noise
Gaussian noise: additive
  observation = signal + noise(standard deviation)
Poisson noise (counts): applied
  Observation = noise(signal)
  Low counts: low noise
  High counts: higher noise (but lower fraction!)
  Converges to gaussian noise
Effect of binning / integrating longer!!

## Slide 5
Convolution
First answer of ChatGPT
def moving_average(y, window_size=5):
return np.convolve(y, np.ones(window_size)/window_size, mode='valid')
y_smooth = moving_average(y, window_size=5)
x_smooth = x[:len(y_smooth)] # adjust x accordingly

## Slide 6
Convolution

## Slide 7
Convolution
First answer of ChatGPT
def moving_average(y, window_size=5):
return np.convolve(y, np.ones(window_size)/window_size, mode='valid')
y_smooth = moving_average(y, window_size=5)
x_smooth = x[:len(y_smooth)] # adjust x accordingly

## Slide 8
Convolution
First answer of ChatGPT
Benefits: simple, same number of points (?)
Problems: edges, window size estimation, shifting (?)
Other suggestions in the answer
  Savitzky-Golay (also window method: next slide)
  Gaussian smoothing (also convolution!)
  Locally weighted regression (I didn’t know this one…)
Other thought: binning (from ~ 3000 points to about 1000 points)
  As long as features are larger than 1 point, this seems like a legit method…
  The statistics are more transparent (in case you want that)

## Slide 9
Savitzky - Golay
Instead of taking the average of points in window, fit a polynomial.
Benefits
very commonly used
Problems?
window size estimation
degree of polynomial
Computationally intensive

## Slide 10
Total Variation methods
Underlying idea
Noise is statistically independent
Signal will be correlated with its neighbors
Allow for ‘sharp edges’ ( = ‘preservation of peaks’)
Our brain does this automagically
Observation(x) = signal(x) + noise(standard deviation)
Note: periodic noise!!!

## Slide 11
Total Variation methods
For images: you want to preserve edges
1992: Post cold-war, declassified!

## Slide 12
Total Variation methods

## Slide 13
Whittaker-Eilers
Apparently, Whittaker had this idea (‘total variation regularization’) earlier
Extended by Eilers in 2004
Here: matrix formalism for fast computation

## Slide 14
Whittaker-Eilers
Note: single point derivative, can also take multipoint derivative
Note: parameter lambda

## Slide 15
Whittaker-Eilers
Note: this is a way to objective determine the value lambda!
The paper then goes into some depth about how to efficiently calculate SCV

## Slide 16
Whittaker-Eilers on our datasets

## Slide 17
Whittaker-Eilers on our datasets
Note: NO parameters,
objective smoother…

## Slide 18
Bonus: Chartrand
u is the derivative of noisy signal f you want to compute.
So you use the integral Au and the derivative u’ of u

## Slide 19
Discussion
Experiences with smoothing?
  Other metrics beyond ‘visually pleasing’?
  In which situations?
  Other methods?
Would you smooth?
  SEM images
  XRD spectra
  FTIR spectra